## Slide 1
Servo Gain Parameter Introduction
By Jim

## Slide 2
1
Self-adjusting
2
Manual Adjusting Parameter
3
CONTENTS
General Commissioning Steps

## Slide 3
Self-adjusting Parameter
01
SECTION

## Slide 4
Self-adjusting
——Load inertia recognition
NOTE: Set servo in position mode(P0-01)

## Slide 5
Self-adjusting
——Load inertia recognition
If there are loud sound and strong vibration during inertia recognition, please reduce the rigidity(P3-02) and then try again.

## Slide 6
Self-adjusting
——Parameter adjustment
Measure the parameters and save the gain result to servo

## Slide 7
Manual Adjusting Parameter
02
SECTION

## Slide 8
Manual Adjusting Parameter
——Position loop gain(P2-01)
Increasing the position loop gain can speed up the positioning time and reduce position deviation. However, too high a setting may lead to system instability and oscillation.

## Slide 9
Manual Adjusting Parameter
——Speed loop gain(P2-02)
With no vibration in the mechanical system, the larger the speed loop gain setting, the better the responsiveness of the servo system and the better the speed following.

## Slide 10
Manual Adjusting Parameter
——Speed loop gain(P2-02)
Small speed loop gain: Have a delayed start and slow stabilization.
Large speed loop gain: Starts quickly and stabilizes quickly, but too large causes system vibration.

## Slide 11
Manual Adjusting Parameter
——Speed loop integral time constant(P2-03)
Used to eliminate velocity loop deviations.
Small gain: improves speed response, too small will cause speed overshoot or vibration;
Large gain: resulting in speed loop bias.

## Slide 12
Manual Adjusting Parameter
——Speed feedforward gain(P2-09)
Used to eliminate errors.
Increase P2-09: further reduce position deviation and improve responsiveness.
Increase too much: lead to overshoot and vibration.
P2-09=0
P2-09=240

## Slide 13
Manual Adjusting Parameter
——Torque filter time constant(P4-04)
Mechanical Resonancce
Normal
Used to suppress mechanical resonance.
The higher the value of this parameter, the stronger the suppression, but setting too large will cause vibration.

## Slide 14
General Commissioning Steps
03
SECTION

## Slide 15
General Commissioning Steps
——Vibration solution
S1: Confirm the source of vibration: whether it is generated by the motor itself or by external interference. (Off enable judgment)
S2: Set the appropriate load inertia ratio(p3-01).
S3: Reduce rigidity level (P03-02).
S4: Adjust torque filtering time constant(P04-04), from the minimum to large.
S5: Adjust the trap, set the trap frequency(P04-05), reduce the trap depth(P04-06) (100: no inhibition. 0: the strongest suppression)
S6: Reduce the input command frequency.
S7: Reduce speed feedforward gain value(P02-09).

## Slide 16
General Commissioning Steps
——Position commissioning steps
S1: Set the appropriate load inertia ratio(P3-01)
S2: Set the speed loop integral time constant(P2-03) as a big value.
S3: Increase speed loop gain(P2-02) until mechanical vibration, take 80% current value.
S4: Reduce speed loop integral time constant(P2-03) until system begin to vibrate.
S5: Increase position loop gain(P2-01) until system begin to vibrate.
S6: If you need shorter positioning time and smaller position devition, you can increase the speed forward gain(P2-09), but should not exceed 80%

## Slide 17
General Commissioning Steps
——Speed commissioning steps
S1: Set the appropriate load inertia ratio(P3-01)
S2: Set the speed loop integral time constant(P2-03) as a big value.
S3: Increase speed loop gain(P2-02) until mechanical vibration, take 80% current value.
S4: Reduce speed loop integral time constant(P2-03) until system begin to vibrate.

## Slide 18: Thank You
www.we-con.com.cn
400 799 8189