## Slide 1
Servo Internal Multi-speed Command
By Jim

## Slide 2
1
Multi-speed Command Introduction
2
DI Terminal Configuration
3
Application
4
CONTENTS
Function Code Configuration

## Slide 3
Multi-speed Command Introduction
01
SECTION

## Slide 4
Multi-segment Postion Mode Introduction
——Application
In this mixer, by adjusting the motor speed, the two materials can be evenly mixed according to the set ratio. Users can set different speed ratios first, and then switch in real time through the DI terminal to suitable the current material ratio.

## Slide 5
Multi-segment Postion Mode Introduction
——Principle
The corresponding speed can be selected through the DI port, max to 8 segments.

## Slide 6
DI Terminal Configuration
02
SECTION

## Slide 7
DI Terminal Configuration
1 DI to enable servo
3 DI to select speed
DI logic&input source selection

## Slide 8
DI Terminal Configuration
Speed Table |  |  | 
15-INSPD3 | 14-INSPD2 | 13-INSPD1 | Speed Command
0 | 0 | 0 | P1-02
0 | 0 | 1 | P1-23
0 | 1 | 0 | P1-24
0 | 1 | 1 | P1-25
1 | 0 | 0 | P1-26
1 | 0 | 1 | P1-27
1 | 1 | 0 | P1-28
1 | 1 | 1 | P1-29

## Slide 9
Function Code Configuration
03
SECTION

## Slide 10
Function Code Configuration
Step 1: Set the running mode
P00-01=2 ——> Speed Control
Step 2: Select the speed command source
P01-01=0 ——> Internal speed command
Step 3: Set the speed command
P01-02=100 P01-23=-100
P01-24=200 P01-25=-200
P01-26=300 P01-27=-300
P01-28=400 P01-29=-400
Step 4: Set the DI terminal
P06-02=1 P06-03=1 P06-04=1
P06-05=13 P06-06=1 P06-07=1
P06-08=14 P06-09=1 P06-10=1
P07-03=15 P06-12=1 P06-13=1
Step 5: Change the DI input
P13-01=1(enable servo) P13-02=xx
P13-03=xx P13-04=xx
Speed Table |  |  | 
15-INSPD3 | 14-INSPD2 | 13-INSPD1 | Speed Command
0 | 0 | 0 | P1-02
0 | 0 | 1 | P1-23
0 | 1 | 0 | P1-24
0 | 1 | 1 | P1-25
1 | 0 | 0 | P1-26
1 | 0 | 1 | P1-27
1 | 1 | 0 | P1-28
1 | 1 | 1 | P1-29

## Slide 11
Application
04
SECTION

## Slide 12
Applition
Step 1: Set the running mode
P00-01=2 ——> Speed Control
Step 2: Select the speed command source
P01-01=0 ——> Internal speed command
Step 3: Set the speed command
P01-02=100 P01-23=-100
P01-24=200 P01-25=-200
P01-26=300 P01-27=-300
P01-28=400 P01-29=-400
Step 4: Set the DI terminal
P06-02=1 P06-03=1 P06-04=1
P06-05=13 P06-06=1 P06-07=1
P06-08=14 P06-09=1 P06-10=1
P07-03=15 P06-12=1 P06-13=1
Step 5: Change the DI input
P13-01=1(enable servo) P13-02=xx
P13-03=xx P13-04=xx
Speed Table |  |  | 
15-INSPD3 | 14-INSPD2 | 13-INSPD1 | Speed Command
0 | 0 | 0 | P1-02
0 | 0 | 1 | P1-23
0 | 1 | 0 | P1-24
0 | 1 | 1 | P1-25
1 | 0 | 0 | P1-26
1 | 0 | 1 | P1-27
1 | 1 | 0 | P1-28
1 | 1 | 1 | P1-29

## Slide 13: Thank You
www.we-con.com.cn
400 799 8189
Form link: https://forms.gle/KrCTWwRXySUuBo4V8